Introducing PCB111000_CP2102

PCB111000_CP2102 is a cut down version of PCB_111000_UNO posted by osbornema on 18 July 2020. It is designed to provide an introduction to C programming for AVR devices and consists of:
A CP2102 module with Rx/Tx and power provided on a 6 pin header
An Atmeg328 for user programs
An ATtiny 1606 that drives an 8 digit seven segment display.

System diagram for PCB111000_CP2102 / The Atmega 328 hosts: / A Hex/text bootloader / An optional UPDI programmer / User programs / Text commentary for several sample / programs. / A default program provided for test / purposes. / The ATtiny1606 / Drives the display / Provides resources for the user projects / One of the switches controls reset and display intensity. The others are or data entry.

System projects

	Name	Compiler	Platform	Task
1	UNO_programs_328	Arduino	UNO	Uploads bootloader and provides time standard for Atmega 328 calibration.
2	UNO_Calibrates_328	Arduino	Atmega328	Calibrates 328 against the UNO crystal
3	CP2102_UPDI_Programmer	Arduino	Atmega328	Uploads mini-OS to ATtiny1606
4	CP2102_mini-OS	Studio 7	ATtiny1606	Drives display and provides user services
5	cal_one_wire_comms	Arduino	Atmega328	Matches 328/1606 baud rates
6	CP2102_bootloader	Studio 7	Atmega328	Loads user projects
7	FP_arithmetic	Arduino	Atmega328	Test project
8	Recal_328_using_crystal	Arduino	Atmega328	Check calibration post pcb assembly

Note: All projects are closely based on previous versions already posted on AVR freaks.
Checking out the operation of the system projects

Operation can be checked out using the prototype system shown below rather than manufacturing and loading a pcb.
Wiring of the prototype system was as follows / (Note photo has error. It shows connection to ATtiny pin 17 instead of pin 18)
UNO		Atmega328		ATtiny1606		CP2102
UNO programs the Atmega328
Pin	Port	Pin	Port	Pin	Port	Port
11	PB3 (MOSI)	17	MOSI
12	PB4 MISO	18	MISO	Note: The CP2102 provides 3.3V logic / However it works with 5V logic / With no load on the 3V3 DC output / the logic is closer to 4V
13	PB5 SCK	19	SCK
A3	PC3	1	Reset
9	PB1	15	Optional LED + 1K detects data download
Atmega328 programs ATtiny1606
		17	PB3 (MOSI)	16	Reset
Atmega328/ATtiny1606 one wire comms
		18	PB4 MISO	18	PA2
Atmega 328 comms
		2	RXD			Tx
		3	TXD			Rx
Atmega 328 control Pin 28 PC5 to 0V via push button switch (the reset control switch) / Plus optional dual LED plus 1K resistors between UNO pins 8 or 9 and 0V
Optional UNO control Reset to GND via temporary wire link (Holds UNO in reset)
UNO +5V: connected to Atmeg328 and ATtiny1606 5V pins / Note: the ATtiny 1606 +5V pin can temporarily be disconnected to reset the device
UNO 0V: connected to the Atmeg328, ATtiny1606 and CP2102 module 0V pins.
CP2102 3.3/5V: No connection

Tests carried out on the prototype system

Connect the UNO to a PC.
Open the UNO app UNO_programs_328 and upload it to the UNO
Open a terminal program and connect (38.4KB)
User prompt s s s s……… should be generated
Connect the CP2102 to the same PC, open a second terminal program and connect (38.4KB).

Operation	User IO
	UNO terminal program	CP2102 terminal program
Calibrate Atmega328 / (UNO generates Pin Change Interrupt every 8.192mS)	Upload / UNO_Calibrates_328. / Send ‘t’ to make program run	1Enter User value for OSCCAL when requested
Upload mini-OS to ATtiny1606	Upload and run / CP2102_UPDI_Programmer	2POR ATtiny1606 / Change baud rate to 14.4K / Send ‘r’, ‘a’, ‘y’, ‘y’ / 3Upload mini-OS
Calibrate the Atmega328 one wire comms clock	Upload and run / cal_one_wire_comms.hex	Change baud rate to 57.6K and press ‘r’ at the user prompt 1Enter cal correction factor when requested
Upload bootloader to Atmega328	Upload and run bootloader.hex / Send P rather than p	4Get user prompt p/r/t/D
Upload and run / Floating_point_numbers: Checks operation of the one-wire link.		Press ‘p’ and send hex file. / Keypress ‘r’ to start then ‘f’ and follow instructions. Press reset control switch on breadboard to reinstate p/r/t/D prompt
Upload commentary		Press T at p/r/t/D prompt / send test.txt
Read commentary		Press t at p/r/t/D prompt / Enter page number then AK

The UNO is used to upload programs to the Atmega328 as follows
Reset the UNO. At the user prompt send ‘s’ then ‘p’ to upload the program and ‘r’ to make it
run unless otherwise stated.
All programs running on the Atmega 328 communicate with the PC via the CP2102.
The ATtiny1606 can only be programmed using CP2102_UPDI_Programmer running on the Atmega328.
Every test can be rerun by resetting the UNO and pressing r or t as required.

1	Back space not supported
2	Power on Reset
3	Trial application requires the display and only works if the one_wire_comms calibration is	adequate.
4	For previously unused devices it may be necessary to pulse the reset control switch or even	repeat the bootloader upload.

Terminal sessions generated while calibrating the Atmega328 are shown below.
Terminal settings are: 8 data bits, 1 stop bit, no parity and no handshaking

Setting up a new PCB111000_CP2102
Before assembling the pcb calibrate the Atmega328 and load it with the bootloader as described above.
Having assembled the pcb:
Connect the pcb to a PC with the vertical switch pressed.
Start a terminal session with the baud rate set to 57.6K.
Check for the presence of the p/r/t/D user prompt

Press ‘p’ and upload CP2102_UPDI_Programmer.
Upload mini-OS
Default user application will run if the one_wire_comms calibration is adequate.

Pulse the vertical switch to restore the p/r/t/D user prompt
Press ‘p’ and upload cal_one_wire_comms.hex
Press ‘r’, ‘r’ to run the program and select a calibration correction factor.
When the program resets press ‘R’ to test the one wire link

Press and hold the vertical switch
Release it while the LEDs are on to reset the program
Release it after the LEDs have gone off to change the display intensity and reset the	program.
Photos of PCB111000_CP2102 / Note that tracks are provided for either surface mount or leaded / Red/Green LED and / watch crystal / The vertical switch is the reset control switch. / The horizontal switches are user switches sw1, sw2 and sw3 / counting from the middle of the pcb. / RX/Tx leds on the CP2102 module have been disabled because they are exceedingly bright.

Use the UNO test jig to calibrate the Atmega328 and load it with the bootloader
Check that the p/r/t/D prompt is generated

Solder on all SM resistors and caps and the 1606
Check the CP2102 module by connecting it to a PC
Add the CP2102 header to the pcb as follows

Solder a 6 pin vertical header to the upper surface
Slide off the plastic spacer
Trim the vertical pins to a length of several mm
Connect the CP2102 module via the header pins
Place a piece of folder paper between the module and pcb
Solder on the module and remove the paper.
Discard the right angled header

Add SM led with 3k9/5k6 series resistors
Add crystal and reset control switch.
Add Atmega328
Power pcb with reset control sw down
connect Bray and get p/r/t/D prompt
press p and upload UPDI programmer

press r at prompt and change baud rate to 14400
press r a y y and upload mini-OS

OSCCAL using Xtal OK
Cal one wire OK
Arithmetic OK
text OK

Add display
Cal one wire plus its app	OK
Default application
First project
Intensity p/r/t/D
POR

Note:
Crystal holes only just large enough
Bright leds:	Remove series resistors on CP2102 module
Increase series resistors on PCB111000 to 3k9/5k6