Full Project commentary
Page 1:

The idea for PCB111000 is based on the ATMEL AVR Butterfly module which came with an excellent text by Joe Pardue (JP) specifically written for the younger beginner. Why not start by downloading the text and skimming through chapters 1 and 2. Rather than the WinAVR compiler we now use Arduino. Programmers notepad (pn) and Bray++ are both still invaluable.

Our first project a simple C program is based on JP’s Blinky, see JP p30. A selection is offered here. Why not choose one and type it in. Click on Sketch then Verify/Compile. Fix the errors it reports (usually typos) then click on Export compiled Binary. Connect the pcb to the computer, open Bray++; set the Baud rate to 57600, click on rescan, then connect. At the user prompt press p, upload the hex file, then press r when the user prompt is reinstated.
Hopefully the display will burst into life.

Look at JP chapter 3 for an intro to Blinky. Now look again at your own code and notice several lines:

#include “First_project_header.h”	This contains additional information required by the compiler, including other .h and .c files with essential definitions and resource subroutines (pn is recommended for opening these).

setup_328_HW (Hard Ware and which is known as (k\a) a macro). Details are given in the header file.

Unsigned int PORT_1	PORT_1 is the name of a memory location that holds numbers. The smallest element of computer memory is a bit and can hold either a 1 or a 0. Memory is often divided into blocks of 8 bits. 16 bits are reserved for PORT_1. It can hold numbers between 0 and 2^16, but excluding 2^16 (2 raised to the power of 16) itself. See JP chapter 4 for an introduction.

One_wire_Tx_2_integers(PORT_1, PORT_1)	This is a resource subroutine which sends data over the one wire link to the ATtiny device which uses it to drive the display.

sei();	This enables interrupts which are required by the one wire link (and will be discussed later)

SW_reset;	This is also a macro. It uses a device k/a a watch dog timer (wtd) to reset the program so that it repeats endlessly.

Having got the example working click on Tools/Auto Format. It makes the code much clearer to read. Why not comment each line stating what it does as a learning aide (See JP p39).

Try several examples, they provide good practice at entering programs. The for loop, the while loop and the if statement are very important features of C. A good look at JP chapter 5: C Control flow is recommended before moving on from this first project.
Of less importance right now are the arithmetic and logic symbols included in the examples. JP gives full definitions of these in chapter 4.

Example 8 introduces the resource subroutines
PRN_16bit_GEN(0) which generates random numbers
Timer_T2_10mS_delay_x_m() which uses a HW timer to generate delays

Example 9 introduces a project subroutine “backup_the_display()”
This provides a service for the main routine
Its main purpose here is to make the code easier to read

Having looked at the examples why not mix and match to compose your own code.

Page 2
Introducing the USART (Universal …. Receiver Transmitter module)
Many devices have a receiver transmitter module for communicating with a PC.
See JP page 98 for a few details.
Arduino provides a comprehensive set of functions for using the USART. Here basic do it yourself (DIY) functions are used. These have been developed after consulting the data sheet which is not nearly as intimidating as it looks at first sight. Studying them helps explain how the USART works. It also demonstrates how other modules such as timers can be set up.

Example 1 simply echoes keypresses to the screen
Example 2 prints many of the common characters to the screen
Clicking on the hex button in the receive section of the Bray window shows that each character is represented by a number. See JP p283.
Example 3 prints a file.
Resource “isCharavailable()” repetitively waits to receive the user to initiate the file upload.
It then notes that the upload has ended and terminates the program.
Example 4 introduces character strings and shows they can be sent to the PC.
It also shows how they are stored in memory.
We compose the strings and choose a name for each one.
 The compiler adds a 0 to the end of each string and replaces its name with the address in memory of the first character in the string.
Example 5 simple prints out the characters together with their numeric equivalents
Example 6 Converts a number to a string of characters and sends them to the PC and
Example 7 Does the reverse.
These are two very important operations So take time to understand what is going on.
See JP pages 81 to 84 for some help.

Finally take a look at the subroutine Char_to_PC()
UCSR0A one of the HW registers that control the UART.
Open the data sheet. In the contents open section scroll down to section 24.12.2
UDRE0 is the name of one of the bits in this register. If it is 0 the UART is busy so we wait
If its 1 we can copy our character to UDR0 the UART data register and it will be transmitted.
Scroll up a bit for more info on the register UDR0.

Page 3
3A looks at timer and keypress interrupts.
Se JP p109 for a general intro.
When driving the display the micro spends most of its time doing nothing waiting for the end of our 100mS delay before updating the display.
In this example the main task is printing out the results of some calculations.
A HW timer is used to generate a 100mS tick.
Every 100mS it interrupts the printing process jumps to the ISR (interrupt service routine) update the display.
In addition a key press interrupt is shown to manipulate the display.

Look at the timer clock_tick() subroutine.
The timer is configured as a counter.
It counts from 0 to 12500
TCCR1B sets a timer clock to 125KHz
So it takes 100ms to complete counting raise an interrupt and start again.

Both timer and UART have control registers that set their modes of operation. These registers have addresses and are all connected to a control bus. A statements like TCCR1B = 0x03 uses the control bus to set register TCCR1B to 3. A bus refers to a set of connectors that transfer data from one part of the micro to another, in this case from the program running in memory to the timer.

Open up the data sheet section 15.11 to see the registers. We leave most of them alone but
set TCCR1B, TIMSK1 OCR1 and TCNT1.

3B looks at interrupts generated by pressing one of the user switches.
PCI stands for pin change interrupt.
Look at the header file for definitions of the macros.
See the data sheet sections 12.2.4 and 1 for detains of the PCI registers.

Note: Many things may look confusing. If that each example successfully introduce one new thing that will be fine.

3C	Nothing new here, just included for a bit if extra practice

3D	Includes PCI and timer as well as the one wire comms interrupt. Multiple interrupts can easily cause trouble. To avoid this the PCI also resets the micro. Before doing so it writes to the EEPROM. After the reset it reads the EEPROM so that it knows whch switch was pressed. EEPROM is a special area of memory that survives power down and reset, which both usually result in all registers being reset to zero.