System file check

31/Aug/2022

PCB_1 updated from Hex file repository

All projects reviewed and given final update

Recompile and check no changes to hex files
cal_one_wire_comms	OK
CP2102_bootloader	OK
CP2102_miniOS	OK
CP2102_UPDI_Programmer	OK
FP_arithmetic	OK
Recal_328_using_crystal	OK
UNO_Calibrates_328	OK
UNO_programs_328	OK

Verification of bootloader hex file	OK

PCB test:

Connect UNO

1.	Open “UNO_programs_328” and upload to UNO
Upload and run UNO_Calibrates_328.
Select User cal as 144	(Default is 145)

2.	Upload and run
CP2102_UPDI_Programmer
Upload mini-OS to ATtiny1606

3.	Upload and run
cal_one_wire_comms.hex
Select one_wire_comms_cal as -10

4.	Upload and run bootloader.hex
Disconnect the UNO
POR PCB111000_CP2102	Default app runs
Pulse reset control switch
Upload “Recal_328_using_crystal”
Select user cal of 143

5.	Power cycle with reset control switch pressed to get the p/r/t/D prompt and press D to get the default application.
Press and hold reset control switch to get high intensity
POR to revert to low intensity
Pulse reset control switch to get p/r/t/D prompt
Upload and run “Floating_point_numbers”

6.	Upload and check commentary:
7.	Upload and run “5E_e_power_series (full)”
Check that the commentary is still OK

Tests
	PCB number
Test	1	2	3	4	5	6	7	8	9	10
1	144/145
2	ok
3	ok
4	143
5	ok
6	ok
7	ok