PCB11000_CP2102

ATtiny 1606			Atmega328

A0 (Reset)	328 PB3		B0	Led
A1	Dig 7		B1	Led
A2(Comms)	328 PB4		B2	n/c
A3	Seg E		B3	Prog output
A4	Seg B		B4	Comms
A5	Dig 3		B5	n/c
A6	Dig 0		B6	n/c Xtal
A7	Dig 1		B7	n/c/Xtal

B0	Dig 4		C0	n/c
B1	Seg A		C1	n/c
B2	Seg D		C2	n/c
B3	Seg DP		C3	n/c
B4	Dig 2		C4	n/c
B5	Seg C		C5	Switch to 0v

C0	Dig 5		D0	RX
C1	Seg F		D1	TX
C2	Dig 6		D2	SW1
C3	Seg G		D3	n/c
			D4	n/c
			D5	SW2
			D6	n/c
			D7	SW3

Reset control

POR	Jump to 0x0000: also resets ATtiny 1606
Short keypress:	Change intensity
Long keypress:	Run bootloader

WDT	Jump to 0x0000 or 0x7000 depending on eeprom setting
Switch	Post User Prompt:	Long press:	Run bootloader
Short press:	Same as POR

Bootloader

Load hex/text programmer at 0x7000.
Load hex verification/text reader at bottom of application partition.

At p/r prompt
Press p to program hex, then jump to hex verification routine, them restore the p/r prompt
Could use wdtout or jump to restore p/r prompt

Press t to program text, then jump to text reader, them restore the p/r prompt
Could use wdtout or jump to restore p/r prompt

Press r to jump to 0x0000.
If 0x0000 contains 0xFFFF jump to default apps.

Issues
Note: pages are erased one at a time just before they are written
Pressing p with erase the first page of the previous application
This should probably be avoided, i.e. wait until hex file down load starts.

Bootloader must be transferred to a Studio application

Jobs

Transfer basic bootloader to Studio app.
Get reset op working as required.
Enhance bootloader to include test and verification.

Tests

In the prototype project “Bootloader_test”:

All resets take program control to location 0x7000.
The setup_HW macro initiates the WDT (clearing the WDRF, bit 3 of MCUSR)
If the POR flag is set control jumps to location 0x0000 (the User application).
If the EXRF is set control continues with the bootloader app.

Project CP2102_bootloader development:

For project CP2102_bootloader:
All resets must take program control to location 0x7000.
If the POR flag is set control must jump to location 0x0000 (the User application).

All resets take control to 0x7000

Post Ext reset:	There is no external reset.

Post WDT	Read WDT flag:
If set: will run bootloader
If clear: Jump to 0x0000.
Post POR{
Clear PORF flag (in MCUSR)
Check SW1
If up:	Do nothing;
If down set WDT flag. (Will run bootloader.)
Initiate WDTout.}

Continue with bootloader
At h/t/r prompt if r is pressed clear WDT flag and initiate WDTout
Clear WDT flag when bootloader completes
Initiate WDTout.

Use of SW1 during execution of user app.
Jump to pin change ISR
Start timer
If short set intensity flag.
If long set WDT flag
Initiate WDTout (to reset 328 or run bootloader)

User App setup_HW macro

Always issues a 1606 reset command and changes intensity if flag is set
Issues intensity command if flag is set
Reset both flags

1606 Reset
POR sets intensity low
Reset command: Issues a WDTout
Intensity command is only active at this moment

328 EEPROM

0x3FF	cal
0x3FE	cal
0x3FD	cal
0x3FC
bit 0	WDT flag	1 for clear and 0 for set
bit 1	Intensity flag

PCB111000_CP2102 Development log

Starting point

UNO driving pcb FP_display_for_UNO_V2	Everything is fine
Load FPN_UNO_app	Runs at 115200 Baud	OK

Replace UNO chip with 328 loaded with Hex/text bootloader (Full hex)

Changes introduced to FP_display_V2:
Internal clock to 1MHz since user projects are now clocked at 8MHz not 16.
Brightness settings to 1450 (definite) and 100 (say)
#define display_tick	4000	to	#define display_tick	2000
#define F_CPU 2000000UL	to	#define F_CPU 1000000UL

Press and hold vertical sw at POR to start bootloader
Switch also controls intensity but not reset
Run Use_projects \Floating_point_numbers All OK

Replace FP_display_V2: with CP2102_miniOS	Works OK with UNO template
Replace UNO_template_V2 with CP2102_UPDI_Programmer
Works OK with	FP_numbers
Proj_1A1
Proj_2C1

Version control Everything running on the FP_display PCB

Use	Github\PCB111000_CP2102\CP2102_bootloader\Full_hex.h
throughout

Put Github_dev\CP2102_UPDI_Programmer\CP2102_UPDI_Programmer.ino.standard
on the 328

Put Github\PCB111000_CP2102\CP2102_miniOS
on the 1606

Run the three use projects stored under
Github\PCB111000_CP2102\User_projects

	FP_display pcb		PCB11000_CP2102
	328	1606	328	1606
Boot loader control SW	PC3	na	PC5 OK	na
UART comms	PC4	PC3	PB4 PCINT4	PA2 OK
Programming	PB3	Reset	PB3 OK	Reset OK

Compare UNO template programmer with UPDI programmer:

OSCCFG fuse
Template is 0x01	Target will run at 16MHz
UPDI programmer is 0x7E	Target will run at 20MHz
Note: Unused bits can be either zero or one

Bug reports

1	See subroutine “ send_int_num()” in
UNO_template_V2\Resources_Template_V2\One_wire_transactions

void send_int_num(long num){
One_wire_Tx_char = 'C';
UART_Tx_1_wire();
for(int m = 0; m <= 3; m++){
One_wire_Tx_char = Long_Num_to_UNO >> (8 * (3 - m));
UART_Tx_1_wire();}}

This should be
void send_int_num(long num){
One_wire_Tx_char = 'C';
UART_Tx_1_wire();
for(int m = 0; m <= 3; m++){
One_wire_Tx_char = num >> (8 * (3 - m));
UART_Tx_1_wire();}}

2	UNO_ARV_Programmer\UNO_AVR_programmer_intro.pdf

See section
UNO_AVR_ programmer Hard Ware:
UNO Tx pin should be connected to Atmega168 pin 3 (USART TXD) and
UNO Rx pin should be connected to Atmega168 pin 2 (USART RXD)