System file check

31/Aug/2022

PCB_1 updated from Hex file repository

All projects reviewed and given final update

Recompile and check no changes to hex files
cal_one_wire_comms	OK
CP2102_bootloader	OK
CP2102_miniOS	OK
CP2102_UPDI_Programmer	OK
FP_arithmetic	OK
Recal_328_using_crystal	OK
UNO_Calibrates_328	OK
UNO_programs_328	OK

Verification of bootloader hex file	OK

PCB test:

Connect UNO

1.	Open “UNO_programs_328” and upload to UNO
Upload and run UNO_Calibrates_328.
Select User cal as 144	(Default is 145)

2.	Upload and run
CP2102_UPDI_Programmer
Upload mini-OS to ATtiny1606

3.	Upload and run
cal_one_wire_comms.hex
Select one_wire_comms_cal as -10

4.	Upload and run bootloader.hex
Disconnect the UNO
POR PCB111000_CP2102	Default app runs
Pulse reset control switch
Upload “Recal_328_using_crystal”
Select user cal of 143

5.	Power cycle with reset control switch pressed to get the p/r/t/D prompt and press D to get the default application.
Press and hold reset control switch to get high intensity
POR to revert to low intensity
Pulse reset control switch to get p/r/t/D prompt
Upload and run “Floating_point_numbers”

6.	Upload and check commentary:
7.	Upload and run “5E_e_power_series (full)”
Check that the commentary is still OK

63
Tests
	PCB number
Test	1	2	3	4	5	6	7	7A	8	9	10
1	144/145	75/129	68/72	146/146	144/144	144/143	60/66	61/63	185/180	136/138	174/169
2	ok	ok	ok	ok	ok	ok	ok	ok	OK
3	-10	-9	-10	-9	-11	-10	-10	-10	-10	-11	-9
4	143	74	67	145	143	143	59	61	184	135	173
5	ok	ok	ok	ok	ok	ok	ok	ok	OK
6	ok	ok	ok	ok	ok	ok	ok	ok
7	ok	ok	ok	ok	ok	ok	ok	ok

PCB Assy
Load all SM resistors/caps and FET
Load CP2102
Load Atmega328
Load Reset control switch
Load Xtal and dual led.

Connect 0V, reset plus programming wires to UNO
Calibrate the Atmega328
Upload UPDI programmer
Upload mini-OS
Cal one wire comms
Upload bootloader

Disconnect UNO
Pulse reset control switch and get p/r/t/d user prompt

Remove UNO wires
Upload FP_arithmetic	OK Led works
Upload Recal_328_using_crystal	OK

Load Display modules

Load user switches

Load the commentary
Project tests

Project	Hex	Operation
1_first_project
1
2
3
4
5
6
7
8
9
10
11
2_Receiver_Transmitter_Basic
1
2
3
4
5
6
7
8
9
3_Interrupts_and_switches
3A_UART_timer_interrupts
3B_Pin_Change_Interrupt
3C_reaction_time_tester
3D_timer_PCI_interrupts
3E_Keypress_logger
3F_Prime_numbers
4_binary_and_bit_operations
1_Bit_ops_1
2_Bit_ops_2
3_Division_subroutine
4_Char_to_binary
5_Arduino_PC_comms_library
5A_Integer_numbers
5B_Prime_factors
5C_Scientific_numbers
5D_Pie_estimator
5E_e_power_series
6_The_8_digit_display_and_IO
6A_Segment_driver
6B_Segment_driver
6C_Numerical_entry
6D_INT_to_display
6E_FPN_to_display
6F_FPN_from_IO
6G_INT_from_IO
7_Timers
1_String_only_clock
2_calculator_based_clock
3_min_OS_clock
4_stand_alone_clock
55_stopwatch
8_Resets
8A_reset_controller
8B_Pulse_train_generator