Introducing PCB111000_CP2102

PCB111000_CP2102 is a cut down version of PCB_111000_UNO published by osbornema on 18 July 2020. It is designed to provide an introduction to C programming for AVR devices and consists of:
A CP2102 module with Rx/Tx and power provided on a 6 pin header
An Atmeg328 for user programs
An ATtiny 1606 that drives an 8 digit seven segment display.

System diagram for PCB111000_CP2102 / The Atmega 328 hosts: / A Hex/text bootloader / An optional UPDI programmer / User programs / Text commentary for several sample / programs. / Two default programs provided for test / purposes. / The ATtiny1606 / Drives the display / Provides resources for the user projects / One of the switches controls reset and display intensity. The others are or data entry.

This project up makes use of the following projects that I have already posted to AVR freaks.
Calibrating the Atmega328 internal RC clock
UNO_AVR programmer
UNO as UPDI programmer
The bootloader used in PCB_111000_UNO
New copies are included in this posting as each project has been modified slightly to fit this application.

For many newcomers to C and microcontroller programming the UNO has probably been an indispensable tool. It is supported by the Arduino development environment and provides:
Communication with a PC
A bootloader for projects
Access to all the IO of an Atmega 328
For me it also provides an easy way of programming and calibrating a number of AVR devices.

However the CP2102 module can also be used to provide communication with a PC. This provides a real incentive to use one of the free PCB design tools and do our designs from scratch. An Atmega preloaded with the Arduino bootloader can be used so nothing else need change. However for project PCB111000_CP2102:
Arduino is used to compile and export user projects
The bootloader is based on the UNO_AVR programmer
A UPDI programmer based on the UNO version is used to program the ATtiny1606
PC communication is made via a terminal program rather than the Arduino GUI.
Setting up a new PCB111000_CP2102

Load a UNO with project “UNO_AVR_programmer”.
Use some solderless breadboard to connect the UNO to an Atmega328.
Program the Atmega328 with the calibration routine and let it run
Program the Atmega328 with the CP2102_bootloader.

Solder the Atmega 328 onto the pcb.

Apply power with the vertical surface mount switch pressed
At the p/r/t prompt press p.
Upload the UPDI programmer
At the p/r/t prompt press r and upload the mini-OS.
Run the test project (appended to the UPDI programmer)
Press the vertical switch (briefly) to obtain the p/r/t prompt

Upload a user project (overwrites the UPDI programmer)
Press the vertical switch releasing it when the led shines to reset both devices
Hold it down until the led goes out to change the intensity.

PCB control

The vertical white surface mount switch controls reset and display intensity as follows:

For a new pcb in which only the bootloader has been programmed power the board with the	switch pressed to operate the bootloader.

Checking out the operation of the code
The prototype system shown below was used develop the code:

Wiring of the prototype system was as follows
UNO		Atmega328		ATtiny1606		CP2102
UNO programs the Atmega328
Pin	Port	Pin	Port	Pin	Port	Port
11	PB3 (MOSI)	17	MOSI
12	PB4 MISO	18	MISO
13	PB5 SCK	19	SCK
A3	PC3	1	Reset
Atmega328 programs ATtiny1606
17	PB3 (MOSI)			16	Reset
Atmega328/ATtiny1606 one wire comms
18	PB4 MISO			17	PA1
Atmega 328 comms
2	RXD					Tx
3	TXD					Rx
Atmega 328 control
28 PC5 to 0V via push button switch
UNO control
GND to reset via temporary wire link
Power
UNO +5V: connected to Atmeg328 and ATtiny1606 5V pins / Note: the ATtiny 1606 +5V pin can temporarily be disconnected to reset the device
UNO 0V: connected to the Atmeg328, ATtiny1606 and CP2102 module 0V pins.
CP2102 3.3/5V: No connection

Test steps

Connect both USB ports to the PC.
Remove reset from the UNO
Open the Arduino sketch “UNO_programs_328_bootloader” .
Upload it to the UNO

Open two terminal programs with default port settings
(8 data bits, no parity 1 stop bit and no flow control).
Change the baud rate to 38.4KB
For each one click on Recsan and connect.
One talks to the UNO and the other the Atmega 328.

The UNO responds by generating the user prompt s s s s s s……..

Press ‘s’ and the programmer should respond with
Atmega 328 detected.
Plus
a number of options.

Calibrating the Atmega328
The Atmega RC clock is calibrated against the UNO crystal.

Press ‘p’ and upload the hex file “UNO_Calibrates_328.ino.standard”
Press ‘t’ to tun the calibration routine
After several seconds the Atmega responds with a number of suitable values for OSCCAL.
Select one from the group with most values registering an error of 0%, i.e. < 1%.

Press the UNO reset button to repeat.

Loading the mini-OS

Change the baud rate of the Atmega 328 terminal program to 14.4KB
Press the UNO reset button
Using the UNO terminal program
Enter ‘s’ then ‘p’ and upload “CP2102_UPDI_Programmer.ino.standard”

Following verification press ‘r’
The Atmega responds with user prompt R? R? R?……….
Enter ‘r’ then ‘a’ the response may be “Power Cycle Required”

If so just
If so press the UNO reset button and use the UNO terminal to enter ‘s then ‘r’
Then power cycle just the ATtiny1606 .
This time use the Atmega terminal program to enter ‘r’, ‘a’, ‘y’, ‘y’ and
upload “CP2102_miniOS” (a Studio 7 file);
Press ‘0’, ‘0’, ‘0’ at the verification phase.

Calibrating the one wire comms link
Both Atmega328 and ATtiny1606 run off free running oscillators.
However no attempt is made to adjust the frequency of the ATtiny1606.
Rather the Atmega328 timer used to generate its comms clock is adjusted to minimise the discrepancy between the two devices. The result is saved to the Atmega328 EEPROM.

Press the UNO reset button and upload “cal_one_wire_comms.standard”

Restore the Atmega terminal baud rate to 38.4KB
and press ‘r’, ‘r’ at the user prompt.

Save the most suitable result.

Always use manufacturing drawings stored on Github when ordering new boards. / Crystal moved to other side if IC and improved power supply wiring and increased separation between pins 11 and 12 of ATtiny1606

PCB11000_CP2102

ATtiny 1606			Atmega328

A0 (Reset)	328 PB3		B0	Led
A1	Dig 7		B1	Led
A2(Comms)	328 PB4		B2	n/c
A3	Seg E		B3	Prog output
A4	Seg B		B4	Comms
A5	Dig 3		B5	n/c
A6	Dig 0		B6	n/c Xtal
A7	Dig 1		B7	n/c/Xtal

B0	Dig 4		C0	n/c
B1	Seg A		C1	n/c
B2	Seg D		C2	n/c
B3	Seg DP		C3	n/c
B4	Dig 2		C4	n/c
B5	Seg C		C5	Switch to 0v

C0	Dig 5		D0	RX
C1	Seg F		D1	TX
C2	Dig 6		D2	SW1
C3	Seg G		D3	n/c
			D4	n/c
			D5	SW2
			D6	n/c
			D7	SW3

Reset control

POR	Jump to 0x0000: also resets ATtiny 1606
Short keypress:	Change intensity
Long keypress:	Run bootloader

WDT	Jump to 0x0000 or 0x7000 depending on eeprom setting
Switch	Post User Prompt:	Long press:	Run bootloader
Short press:	Same as POR

Bootloader

Load hex/text programmer at 0x7000.
Load hex verification/text reader at bottom of application partition.

At p/r prompt
Press p to program hex, then jump to hex verification routine, them restore the p/r prompt
Could use wdtout or jump to restore p/r prompt

Press t to program text, then jump to text reader, them restore the p/r prompt
Could use wdtout or jump to restore p/r prompt

Press r to jump to 0x0000.
If 0x0000 contains 0xFFFF jump to default apps.

Issues
Note: pages are erased one at a time just before they are written
Pressing p with erase the first page of the previous application
This should probably be avoided, i.e. wait until hex file down load starts.

Bootloader must be transferred to a Studio application

Jobs

Transfer basic bootloader to Studio app.
Get reset op working as required.
Enhance bootloader to include test and verification.

Tests

In the prototype project “Bootloader_test”:

All resets take program control to location 0x7000.
The setup_HW macro initiates the WDT (clearing the WDRF, bit 3 of MCUSR)
If the POR flag is set control jumps to location 0x0000 (the User application).
If the EXRF is set control continues with the bootloader app.

Project CP2102_bootloader development:

For project CP2102_bootloader:
All resets must take program control to location 0x7000.
If the POR flag is set control must jump to location 0x0000 (the User application).

All resets take control to 0x7000

Post Ext reset:	There is no external reset.

Post WDT	Read WDT flag:
If set: will run bootloader
If clear: Jump to 0x0000.
Post POR{
Clear PORF flag (in MCUSR)
Check SW1
If up:	Do nothing;
If down set WDT flag. (Will run bootloader.)
Initiate WDTout.}

Continue with bootloader
At h/t/r prompt if r is pressed clear WDT flag and initiate WDTout
Clear WDT flag when bootloader completes
Initiate WDTout.

Use of SW1 during execution of user app.
Jump to pin change ISR
Start timer
If short set intensity flag.
If long set WDT flag
Initiate WDTout (to reset 328 or run bootloader)

User App setup_HW macro

Always issues a 1606 reset command and changes intensity if flag is set
Issues intensity command if flag is set
Reset both flags

1606 Reset
POR sets intensity low
Reset command: Issues a WDTout
Intensity command is only active at this moment

328 EEPROM

0x3FF	cal
0x3FE	cal
0x3FD	cal
0x3FC
bit 0	WDT flag	1 for clear and 0 for set
bit 1	Intensity flag

Bug reports

1	See subroutine “ send_int_num()” in
UNO_template_V2\Resources_Template_V2\One_wire_transactions

void send_int_num(long num){
One_wire_Tx_char = 'C';
UART_Tx_1_wire();
for(int m = 0; m <= 3; m++){
One_wire_Tx_char = Long_Num_to_UNO >> (8 * (3 - m));
UART_Tx_1_wire();}}

This should be
void send_int_num(long num){
One_wire_Tx_char = 'C';
UART_Tx_1_wire();
for(int m = 0; m <= 3; m++){
One_wire_Tx_char = num >> (8 * (3 - m));
UART_Tx_1_wire();}}

2	UNO_ARV_Programmer\UNO_AVR_programmer_intro.pdf

See section
UNO_AVR_ programmer Hard Ware:
UNO Tx pin should be connected to Atmega168 pin 3 (USART TXD) and
UNO Rx pin should be connected to Atmega168 pin 2 (USART RXD)