Example 3A / Timer/Receiver signals interrupt main routine			ISR / Interrupt Service Routine
Main routine: / Clock routine: / Timer ISR: / Receiver ISR:	Generates and sends data to PC / Generates interrupt stream / Drives the display / Manual display control	ISR(TIMER1_OVF_vect) / {UCSR0B &= (~(1 << RXCIE0)); / TCNT1 = 0xCF2C; / if(m < num_leds) / {PORT_2 = (PORT_2 << 1) | 1; / PORT_1 = PORT_1 & (~(1<< m));} / else / {PORT_2 = (PORT_2 >> 1); / PORT_1 |= (1 << (num_leds * 2 - m -1));} / for(int m = 15; m >=num_leds; m--) / PORT_1 &= ~(1 << m); / sei();One_wire_Tx_2_integers(PORT_1, PORT_2); / m += 1; / if (m==num_leds * 2)m=0; / UCSR0B |= (1 << RXCIE0);}
#include "UART_timer_interrupt_header.h" / int m, num_leds = 8; / unsigned int PORT_1, PORT_2; / int main (void) / {unsigned long counter=1; / unsigned long counter_squared; / setup_328_HW; / reset_display; / sei(); / UCSR0B |= (1 << RXCIE0); / T1_100ms_clock_tick(); / while(1) / {do_some_arithmetic;}}

		ISR(USART_RX_vect) / {switch(Char_from_PC()) / {case '2': num_leds = 2; break; / case '4': num_leds = 4; break; / case '6': num_leds = 6; break; / case '8': num_leds = 8; break; / case 'A': num_leds = 10; break; / case 'C': num_leds = 12; break; / case 'E': num_leds = 14; break; / case '0': num_leds = 16; break;} / reset_display;}
void T1_100ms_clock_tick(void) / {TCNT1 = 0xCF2C; / TIMSK1 |= (1 << TOIE1); / TCCR1B = 0x03;}

Example 3B: A first reaction time tester / Shooting down the leds / Switch presses interrupt the main routine
Main routine: Drives the display / Switch 2 (middle Sw) manipulates the display	int main (void) / {setup_328_HW; / set_up_PCI_on_sw2; / enable_pci_on_sw2; / mask = 0xFFFF; / sei(); / while(mask) / {scan = 1; / PORT_1=1; / while(scan) / {if(PORT_1 == 1)switch_control = 0; / One_wire_Tx_2_integers / (PORT_1 & mask, (~mask) ^ PORT_1); / Timer_T2_10mS_delay_x_m(2); / if(PORT_1 & 0x8000)scan = 0; / else / PORT_1 = (PORT_1 << 1);}} / One_wire_Tx_2_integers(0, 0xFFFF); / Timer_T2_10mS_delay_x_m(200); / SW_reset;}
#include "Pin_Change_Interrupt_header.h" / unsigned int PORT_1, mask; / char scan; / char switch_control; / ISR(PCINT2_vect) / {if(switch_2_up)return; / if(switch_control) return; / if(mask & PORT_1) / {mask &= ~PORT_1; / scan = 0;} / switch_control = 1;}

Example 3C Second Reaction time tester / Nothing new: Press sw2 to start and release it immediately that the leds line up.	Example 3D / Combines Timer and switch press interrupts with one wire comms interrupt
int main (void) / {unsigned int Random_num; / unsigned int PORT_1, PORT_2; / setup_328_HW; / while(switch_2_up); / PORT_1=1; / PORT_2=0x8000; / while (1) / {while(1) / {Timer_T2_10mS_delay_x_m(1); / while(switch_2_up); / shift_PORT_1; / shift_PORT_2; / One_wire_Tx_2_integers(PORT_1, PORT_2); / if(PORT_1 == PORT_2) / {Timer_T2_10mS_delay_x_m(35); / if(switch_2_up)break; / else while(switch_2_down);} / if(PORT_1 != PORT_2) / {Timer_T2_10mS_delay_x_m(8);}} / while(switch_2_up) / {flash_display;}}}	#include "Timer_PCI_header.h" / volatile char T1_OVF; / unsigned int n, n_max; / long PORT_1,PORT_2; / char p = 0; / char mode = 1; / int main (void) / {setup_328_HW; / mode = eeprom_read_byte((uint8_t*)0); / switch (mode) / {case 0: case 1: case 2: break; / default: mode = 0; break;} / set_up_PCI; / enable_PCI; / T1_OVF = 0; / sei(); / T1_100ms_clock_tick(); / initialise_display(); / while(1) / {while(!(T1_OVF)); T1_OVF = 0; / Inc_Display();}} / ISR(TIMER1_COMPA_vect) / {OCR1A += 0x30D4; T1_OVF = 1;} / ISR(PCINT2_vect) / {if((switch_1_up) && (switch_2_up) && (switch_3_up)){ / return;} / if(switch_1_down) eeprom_write_byte((uint8_t*)0x0, 0); / if(switch_2_down) eeprom_write_byte((uint8_t*)0x0, 1); / if(switch_3_down) eeprom_write_byte((uint8_t*)0x0, 2); / SW_reset;} / void T1_100ms_clock_tick(void) / { TCNT1 = 0; / OCR1A = 0x30D4; / TIMSK1 |= (1 << OCIE1A); / TCCR1B = 0x03;}