Example 3A / Timer/Receiver signals interrupt main routine			ISR / Interrupt Service Routine
Main routine: / Clock routine: / Timer ISR: / Receiver ISR:	Generates and sends data to PC / Generates interrupt stream / Drives the display / Manual display control	ISR(TIMER1_OVF_vect) / {UCSR0B &= (~(1 << RXCIE0)); / TCNT1 = 0xCF2C; / if(m < num_leds) / {PORT_2 = (PORT_2 << 1) | 1; / PORT_1 = PORT_1 & (~(1<< m));} / else / {PORT_2 = (PORT_2 >> 1); / PORT_1 |= (1 << (num_leds * 2 - m -1));} / for(int m = 15; m >=num_leds; m--) / PORT_1 &= ~(1 << m); / sei();One_wire_Tx_2_integers(PORT_1, PORT_2); / m += 1; / if (m==num_leds * 2)m=0; / UCSR0B |= (1 << RXCIE0);}
#include "UART_interrupt_header.h" / int m, num_leds = 8; / unsigned int PORT_1, PORT_2; / int main (void) / {unsigned long counter=1; / unsigned long counter_squared; / setup_328_HW; / reset_display; / sei(); / UCSR0B |= (1 << RXCIE0); / T1_100ms_clock_tick(); / while(1) / {do_some_arithmetic;}}

		ISR(USART_RX_vect) / {switch(Char_from_PC()) / {case '2': num_leds = 2; break; / case '4': num_leds = 4; break; / case '6': num_leds = 6; break; / case '8': num_leds = 8; break; / case 'A': num_leds = 10; break; / case 'C': num_leds = 12; break; / case 'E': num_leds = 14; break; / case '0': num_leds = 16; break;} / reset_display;}
void T1_100ms_clock_tick(void) / {TCNT1 = 0xCF2C; / TIMSK1 |= (1 << TOIE1); / TCCR1B = 0x03;}

Example 3B: A first reaction time tester / Switch presses interrupt the main routine
Main routine: Drives the display / Switch 2 (middle Sw) manipulates the display	int main (void) / {setup_328_HW; / set_up_PCI_on_sw2; / enable_pci_on_sw2; / mask = 0xFFFF; / sei(); / while(mask) / {scan = 1; / PORT_1=1; / while(scan) / {if(PORT_1 == 1)switch_control = 0; / One_wire_Tx_2_integers / (PORT_1 & mask, (~mask) ^ PORT_1); / Timer_T2_10mS_delay_x_m(2); / if(PORT_1 & 0x8000)scan = 0; / else / PORT_1 = (PORT_1 << 1);}} / One_wire_Tx_2_integers(0, 0xFFFF); / Timer_T2_10mS_delay_x_m(200); / SW_reset;}
#include "Pin_Change_Interrupt_header.h" / unsigned int PORT_1, mask; / char scan; / char switch_control; / ISR(PCINT2_vect) / {if(switch_2_up)return; / if(switch_control) return; / if(mask & PORT_1) / {mask &= ~PORT_1; / scan = 0;} / switch_control = 1;}